## Slide 1: Graphics on the Commodore 64
Graphics on a 16kb Shoestring Budget
by
DeeKay/Crest
Apr 15th, 2006

## Slide 2: Part 1
Meet the Pixels

## Slide 3: Basics
PAL-VIC: 312 Rasterlines, no halfpictures (identical lines in both half-pictures)
4 Banks à 16KB, all displayed VIC-data needs to be within the same bank (Bitmap, Chars, Sprites)
Rasterbeam goes linewise from the top left to the lower right, VIC also works that way
320x200 screen plus border (2 sprites=6 chars each on left/right, about 2 sprites upper/lower)

## Slide 4: Basics
Palette of 16 Colors, fixed
1 Char (Character) = 1 CPU-cycle
No direct adressing of pixels

## Slide 5: Some important VIC-Registers you should remember:
$d020: Border color
$d021: Screen color
$d022/23: Multicolors
$d016: X-shift Register
$d012: Rasterbeam counter
$d011: Good for a great many things (VIC-tricks)

## Slide 6: Lingo
“Char”: One 8x8 pixel block (doesn’t matter if it’s actually char-mode!)
“MSB”: Most Significant Bit: To cover overflow of an x/y value above $ff
“Border”: The “outer safe frame” area surrounding the screen (made to compensate for various different TVs and monitors)
“Koala”: synonymous for Multicolor Bitmap, named after a program called “Koala Painter”

## Slide 7: Displaying Graphics
Standard Bitmap
Character Set
Sprites
Advanced (but fairly useless) Stuff: Ghost-Byte, $d016

## Slide 8: Graphic Modes
Hires: square Pixels: two colors, 8x8 pixels/char
Multicolor: 2 bpp, four colors : 4x8 pixels/char
$d021: Bitpattern 00
$d022/Hi-Nibble (ScreenRAM): Bitpattern 01
$d023/Low-Nibble (ScreenRAM): Bitpattern 10
$d800 (”ColorRAM”): Bitpattern 11

## Slide 9: Standard Bitmap
Hires 320*200, Multicolor 160*200
Divided into 40*25 Chars (8*8 Hires-pixels),
char-sequential: no linear adressing!
8000 Bytes = $2kb
Fixed positions in RAM: $0000, $2000 etc.
Changeable by bank-switching

## Slide 10: Standard Bitmap Hires/Multicolor
Hires: 2 colors per char, colors are stored in ScreenRAM
ScreenRAM: length $0400, fixed positions in active bank: $x000, $x400, $x800, $xc00 etc., colors are high and low nibble
Multicolor: 4 colors per char, ScreenRAM + ColorRAM + Background ($d021)
ColorRAM: length $0400, always on $d800, low-nibble only

## Slide 11: Sprites
24*21 pixels (hires) = 63 bytes
sequential byte-order by line, no chars
8 sprites, can be multiplexed (horizontally no more than 8)
Multicolor/Hires can be set individually per sprite
Hires: one color plus transparent background
Multicolor: 3 colors plus transp. background, 2 colors fixed for all sprites, one individual color per Sprite

## Slide 12: Sprites
Can be expanded to twice the width and/or height (pixels scale accordingly)
Collision between sprites or sprites and chars can be detected
Trickery! Sprite 1 can be behind Bitmap/Char, but above Sprite 2 which itself is above the bitmap. This essentially cuts a hole in Sprite 2 letting the bitmap shine through -> EOR-effects and more!

## Slide 13: Sprite-”Cookiecutter”
Sprite 1 still in front of Sprite 2 (but behind Background!)
Sprite 1 in front of Background and Sprite 2

## Slide 14: Sprite-Priority
Sprites can be above or behind bitmap/chars
Behind set bits in hires, in Multicolor only behind $d023 (or ScreenRAM Low-Nibble) & $d800 (ColorRAM)
Tricks possible with covering

## Slide 15: Charset
256 characters per char, 8 bytes per character, sequential store by 8*8 char
Length: $0800
Located on $x000, $x800, $xc00 of active bank
Hires: One color out of 16 per char (ColorRAM)
Multicolor: 2 fixed colors + $d021 + ColorRAM (only first 8 colors, second 8 are the same only in hires)

## Slide 16: Charset
Screen for charset: same as ScreenRAM in Bitmap, on $x400 boundaries
New mode besides Multicolor/Hires: ECM: 64 Hires-Chars where each can have one of 4 different background colors (Multicolor-Registers, $d021-24). On top of that is each char’s ColorRAM.

## Slide 17: Making Graphics on the C64
16 Colors
Many ways to go from black to white: Lots of possible transitions
Seven Color-Pairs with same luminance for all colors plus black and white (a/c/e/5: special case!)
sensible choice of colors for each char: choose colors that you can use often, don’t use colors from the same pair if you’re starved of colors

## Slide 18: Making Graphics on the C64
Don’t choose the most often used color as $d021, choose the color that you can use as substitute most often: No black, no white, cannot be used as substitute or for Antialiasing. Good choice because color-less: One of the 3 greys
Predominantly for Bitmap, but same goes for choice of Sprite- and Char-Multicolors

## Slide 19: Old VIC special
Very early C64s have a different VIC. Only five different luminances instead of nine
Many colors are the same luminance -> Color-fades look worse
Not very many in existence, so dont worry too much
Ask Widdy! ;-)

## Slide 20: Advanced c64-Graphics
Most advanced graphicmodes can be reached through various tricks that change VIC-registers at the right time while the graphic is being displayed (c64 version of Pixelshaders! ;-)
More colors or higher resolution, but hard to use in Demoparts with compute-intensive Effects, because it takes away rastertime while GFX is being displayed

## Slide 21: Advanced c64-Graphics
FLI: Flexible Line Interpreter, two new colors (ScreenRAM) every line instead of every 8th line, has FLI-Bug (solid light grey, 3 chars wide) at the left of the screen, either Hires (AFLI or Hi-FLI) or Multicolor; Editors: Blackmail/CPU Editor, FLIP
IFLI: Interlaced FLI, same as FLI Multicolor, only interlaced (2 screens alternating) and with a 1-pixel x-shift every frame to give it a pseudo-hires look; Editors: Funpaint, Gunpaint

## Slide 22: Advanced c64 Graphics
Sprites overlay modes: SHF, SHIF (SHF interlace), SHF-XL: Hires-FLI-Bitmap with sprite-layer(s) over it for more colors; dont cover the whole screen, but are very high resolution; Editors: Crest SHF/SHIF/SHF-XL Editor
Sprite underlay modes: UFLI and UIFLI (UFLI Interlace): X-expanded Hires-sprite-layer (twice as wide pixels) underneath the set pixels of a Hires-FLI-Bitmap (FLI every second line only); High resolution, fairly colorful, covers almost the full screen

## Slide 23: Advanced c64-Graphics
Border-GFX: VIC knows 23x38 char border for smooth scrolling. Fool the VIC by changing the registers into believing it switched on the border already when the rasterbeam reaches the border
Open border has limited GFX-capabilities: Only $d021 & sprites, no chars, no standard bitmap, only one black repeating hires Ghostbyte in the upper/lower border (last Byte in the active Bank) plus one $d016-byte when you tear open $d021

## Slide 24: Free Advanced Graphic Modes
Advanced GFX-modes can be done without FLI, meaning the rastertime while the graphic is displayed can be used for other things.
No FLI means less colors
Sprite-overlay/underlay with Bitmap: Standard Bitmap (Multicolor or Hires), only Sprites need to be multiplexed every 21 Rasterlines
Drazlace: Interlaced normal Bitmaps, with or without $d016 1-Pixel-x-shift

## Slide 25: Linear Framebuffer
How can I output my Code without the hassle of adressing the non-linear structure of c64-gfx?
A nearly linear framebuffer can be emulated with various tricks, mostly in the end being some sort of a 4x4 pixel structure and 1/4 FLI.
Some effects can be emulated with avoiding heavy calculation and relying on VIC-tricks instead, mostly also using Hi-Res graphics..

## Slide 26: Examples of c64 Graphics
Hooray! Pwetty pictures time!

## Slide 27: Examples
Standard 4-color GFX (most often char)

## Slide 28: Examples
Standard Multicolor (160x200, no interlace)

## Slide 29: Examples
Standard Multicolor, non-interlaced

## Slide 30: Examples
FLI Multicolor, non-interlaced

## Slide 31: Examples
Interlaced FLI

## Slide 32: Examples
Interlaced FLI

## Slide 33: Examples
Multicolor Interlace aka Drazlace (”free” advanced mode!)

## Slide 34: Examples
UFLI (320x200, 1/2 Hires-FLI plus Sprite-Layer)

## Slide 35: Examples
Hires-FLI
Super-Hires-Interlace FLI (SHIF, Interlaced Hires-FLI with 2 Hires Sprite-Layers, 96x112 pixels only)

## Slide 36: Examples
UIFLI: UFLI Interlace, the Crest of c64 Graphics: Very many colors, awesome transitions, much detail, covers whole screen

## Slide 37: c64 Graphics with PC/Mac
Pixelling, converting and displaying

## Slide 38: Areas of usage
Do Screendesigns for your coders!
Display c64-Graphics with Xnview (Lin/Mac/Win), ACDsee+Plugins (Win), ShowVIC or various plugins on Amiga
Do special graphics where editors do not exist on c64 on PC/Mac
Pixel c64-Graphics with Timanthes or Elitepaint (Win)
Use PC-Programs to do tedious/impossible jobs
PC/Mac can be a great tool

## Slide 39: Convert stuff
Various converters available for all kinds of graphics modes (konv1.exe, BigVIC, Raydomat, ProjectOne, Timanthes etc)
Be fair - Don’t just convert readymade pictures by others and hand them in for the compo!
Fix errors on the c64, converting is never as good as hand-pixelling

## Slide 40: Making graphics in special modes
Good coders WILL ask you to do graphics in 10x300 pixels with one new color every 5 characters and grey in all uneven lines - but only when the moon is full!
Since the limitations are normally very uncommon, editors usually don’t exist on c64
If possible, use Photoshop and other tools to emulate these features - be creative!

## Slide 41: Making graphics in special modes
Example: A texture with 3 colors in every line
Solution: Use Photoshop with 3 layers filled with only lines of one color, mask them and paint in the masks in b/w with a 2-pixel wide brush

## Slide 42: Making graphics in special modes
Example 2: A sprite-logo (24 chars wide) with one new color every line
Solution: Fill outlines with rasterbars, adjust remaining colors for needed additional fixes...

## Slide 43: Making graphics in special modes
Making Sideborder GFX in Photoshop for lack of a suitable Editor

## Slide 44: Screendesigns
Version 1 Version 2
Version 3 Final part

## Slide 45: Pattern-making
Use Photoshop Functions to make background-patterns etc.

## Slide 46: The End
Thank you for watching!

## Slide 47: Glossary
Multicolor FLI: also called “FLI”
Multicolor Bitmap: also called “Koala”, “Amicapaint”, “Paintmagic”
IFLI: Also “Funpaint”, “FLI Interlace”, FLInt or “Gunpaint”
Hires-FLI: Also called “Hi-FLI” or “AFLI”